## Slide 1: Primary CPU function
The Four Primary Functions of the CPU:
The CPU processes instructions it receives in the process of decoding data. In processing this data, the CPU performs four basic steps:
Fetch Each instruction is stored in memory and has its own address. The processor takes this address number from the program counter, which is responsible for tracking which instructions the CPU should execute next.
Decode All programs to be executed are translated to into Assembly instructions. Assembly code must be decoded into binary instructions, which are understandable to your CPU. This step is called decoding.
Execute While executing instructions the CPU can do one of three things: Do calculations with its ALU, move data from one memory location to another, or jump to a different address.
Store/Write Back The CPU must give feedback after executing an instruction and the output data is written to the memory.

## Slide 2
Machine Cycle /Instruction Cycle

## Slide 3: CPU’s Basic Term
Instruction (command): is a sequence of 0s and 1s that describes a physical operation the computer is to perform (such as "ADD“, “LOAD”)
Instruction set : An instruction set is a group of commands for a CPU in machine language.
Instruction Cycle: time taken to complete one Instruction
Clock cycle: A complete pulse. 2GHz that means 2×10^9 pulse or 2×10^9 Clock cycle
Clock Speed: Cycles per second

## Slide 4: CPU Architecture
There are two types of CPU architecture:
CISC: Complex Instruction Set Computer/computing
RISC: Reduce Instruction Set Computer/computing
Each Architecture has machine code that correspond with their own unique assembly language.

## Slide 5: Instruction Set Architecture(ISA)
ISA allows communication between hardware and software. It is also a group of command for a CPU machine language.
Command or Instruction: also opcode or instruction code
There are two types of ISA:
CISC
RISC

## Slide 6: CISC Vs RISC
 | CISC | RISC
 | Mostly found in laptop and desktop where multiple larger task run at a time | Tablet, Phone, in a word consumer product and embedded system
 | Larger number of Instruction set (using basic instruction built in a lot of complex instruction) | Laser set of instruction (only basic instruction)
 | To product A and B that means A*B Instruction set: MULT A,B | Instruction set: LOAD R1, A LOAD R2, B PROD A,B Store R3, A
Instruction Set (CISC>RISC) | More than RISC | Less than CISC
 | Emphasis on hardware | Emphasis on software

## Slide 7: CISC Vs RISC
Execution time | Multiple number of cycle per instruction | One cycle per instruction
CPU SIZE (CISC>RISC) | Larger CPU Because: it has larger instruction set(library) and installed fan on CPU for cooling it | Lesser CPU
 |  | RISC CPU Light and portable And can be put into single chip
 | Consume greater energy | Lower energy required
SPEED | CBC takes a while to process the instruction | Where as RISC CPU will: Just do it
Task size | CISC are more capable in handling intensive task which makes it batter for large variety of tasks. | RISC can only perform simple task quicker than CISC

## Slide 8: CISC Vs RISC
Who is winner?
Ans: Both of CISC and RISC
Why?
Both are suitable of its specific application.

## Slide 9
Now both of CISC & RISC are used in many system.
And its called Explicitly Parallel Instruction Computer(EPIC).
That means, CISC+RISC=EPIC.

## Slide 10
Example:
Main Memory (RAM)
 | 1 | 2 | 3 | 4 | 5 | 6
1 | 1,1 | 1,2 | 1,3 | 1,4 |  | 
2 | 2,1 | 2,2 | 2,3 |  |  | 
3 | 3,1 | 3,2 | 3,3 |  |  | 
4 | 4,1 | 4,2 | 4,3 |  |  | 
A | D
B | E
C | F
+ - × ÷