## Slide 1: IoT Army of 300
Resource Development to enable Our Brightest Minds in Technology
Abdur Rahman
Lecture 2
Introduction to Atmega32
Oct 16, 2017

## Slide 2: Atmega32 features
High-performance, Low-power Atmel®AVR® 8-bit Microcontroller
Memory
    32KB Flash memory: program memory
    1KB EEPROM: Data momory
    2KB SRAM: Store the value of variable
    Register memory:
Write/Erase Cycles: 10,000 Flash/100,000 EEPROM
Operating Voltages : 4.5V - 5.5V
Speed Grades: 0 - 16MHz for ATmega32

## Slide 3: PINOUT
Total pin: 40
4×8=32 I/O pin
4 I/O PORT
PORTA 8 pins
PORTB 8 pins
PORTC 8 pins
PORTD 8 pins
10 bit, 8 channel ADC

## Slide 5: I/O Control Registers
DDRx – Controls the output tristate for port x
  DDRx bit = 1 makes the port x an output pin
  DDRx bit = 0 makes the port x an input pin
  Ex. DDRA = 0b11001100, outputs are bits 7, 6, 3, and 2
PORTx – Control the value driven on port x
  Only meaningful if port x is an output
  Ex. PORTA = 0b00110011 assigns pin values as shown
PINx – Contains value on port x
  Ex. Q = PINC;

## Slide 6: Typical Embedded C Program
#include <stdio.h>
main() {
// initialization code
while (1) {
// main code
}
}
#include is a compiler directive to include (concatenate) another file
main is the function where execution starts

## Slide 7: C Syntax Basics
Comments: single line //, multiline /* … */
Semicolon used to terminate all statements
# indicates a compiler directive (include, define, etc.)
Brackets { … } group lines of code for execution
Blankspace between lines is not important in C
  Still need to separate tokens
int a, b, c;
a = b + c;
int a,b,c;a=b+c;
inta,b,c;a=b+c;
correct
incorrect (inta)
correct

## Slide 8: Variables
All variables’ types must be declared
  Memory space requirements known statically
  Type checking can be performed at compile-time
Numerical Types: int, float, double
Other types: char, void
Type qualifiers: short, long, unsigned, signed, const
  Specify alternate sizes, constrain use modes

## Slide 9: Variable Declaration
Static allocation vs. Dynamic allocation
Static dedicates fixed space on the stack
  int i;
Dynamic (malloc) allocates from the heap at runtime
  ptr = malloc(32);
Type sizes depend on the architecture
  On x86, int is 32 bits
  On ATmega2560, int is 16 bits
  char is always 8 bits

## Slide 10: Volatile Variables
The value of a volatile variable may change at any time, not just at an explicit assignment
Also, may be read at any time
Compiler optimizations are not applied to volatile variables
for (i=0; i<10000; i++);
An optimizing compiler would delete this loop
  i is not used anywhere in the code
i = 1; … i = 1;
If i is not modified in between, the second assignment is removed

## Slide 11: Volatile Variables
When can variables be used without an explicit assignment?
1. Memory-mapped peripheral registers
2. Global variables modified by an interrupt service routine
3. Global variables accessed by other processors

## Slide 12: Volatile Example
.
.
while (*periph != 1); // wait until data transfer
. // is complete
.
periph is the mapped address of the peripheral status info
*periph is assigned by peripheral directly
Compiled code will move memory contents to a register
Memory will only be moved once because *periph does not change

## Slide 13: Base Representation
Base 10 is default
Base can be specified with a prefix before the number
Binary is 0b, Hexadecimal is 0x
  Ex. char x = 0b00110011;
  char x = 0x33;
Binary is useful to show each bit value
Hex is compact and easy to convert to binary
  1 hex digit = 4 binary digits

## Slide 14: Types of Statements
Assignment – =
Relational - <, >, ==, !=
Control Flow – if, for, while, do, switch
Arithmetic Operations - +, -, *, /, %
Logical Operations - &&, ||, !
Bitwise Logical Operations - &, |, ^

## Slide 15: Logical Operators
These operators accept binary input and produce binary output
&&, ||, !
Non-binary inputs are cast to binary values
int a=1, b=0; c=56; d=-1, res;
res = a && b; // res = 0
res = a || b; // res = 1
res = c && d; // res = 1

## Slide 16: Bitwise Operations
Treat the value as an array of bits
Bitwise operations are performed on pairs of corresponding bits
X = 0b0011, Y = 0b0110
Z = X | Y = 0b0111
Z = X & Y = 0b0001
Z = X ^ Y = 0b0101
Z = ~X = 0b1100
Z = X << 1 = 0b0110
Z = x >> 1 = 0b0001

## Slide 17: Bit Masks
Need to access a subset of the bits in a variable
  Write or read
Masks are bit sequences which identify the important bits with a ‘1’ value
Ex. Set bits 2 and 4 in X, don’t change other bits
  X = 01010101, mask = 0010100
  X = X | mask
Ex. Clear bits 2 and 4
  mask = 11101011
  X = X & mask

## Slide 18: Bit Assignment Macros
1 << (n) and ~(1) << (n) create the mask
  Single 1 (0) shifted n times
Macro doesn’t require memory access (on stack)
#define SET_BIT(p,n) ((p) |= (1 << (n)))
#define CLR_BIT(p,n) ((p) &= (~(1) << (n)))

## Slide 19: Header Files
Files included at the top of a code file
Traditionally named with .h suffix
Include information to be shared between files
  Function prototypes
  externs of global variables
  Global #defines
Needed to refer to libraries

## Slide 20: Compilers/IDE for AVR
WinAVR free
Atmel Studio free
Micro c pro for AVR paid
Simulator:
proteus 8.1

## Slide 21
Local IP: 192.168.2.133
Public IP: 182.48.84.180