## Slide 1: IoT Army of 300
Resource Development to enable Our Brightest Minds in Technology
Abdur Rahman
Lecture 4
Lecture_4 Bitwise operator & Operation
Nov 15, 2017

## Slide 2: Exam1 : Syllabus
  Microcontroller (MCU)??
    PC Vs MCU
    Performance measurement factors
  Atmega32 ??
    PinOut
    I/O registers
    Output Operation , LED Blinking
    Input Operation, Button Interfacing
  Bitwise operators & its implementation
  Macros

## Slide 3: Very low-level stuff
Bitwise operations in C
Slides created by:
Abdur Rahman
abdurrahman.iit@gmail.com

## Slide 4: Bitwise Operations
Treat the value as an array of bits
Bitwise operations are performed on pairs of corresponding bits
  AND (&)
  OR (|)
  XOR (^)
  NOT (~)
  Right shift (>>)
  Left shift (<<)

## Slide 5: Bitwise Operations
C contains six operators for performing bitwise operations on integers:
  & Logical AND: if both bits are 1 the result is 1
  | Logical OR: if either bit is 1, the result is 1
  ^ Logical XOR (exlusive OR): if and only if total number of bits(1) are odd, the result is 1
  ~ Logical invert: if the bit is 1, the result is 0; if the bit is 0, the result is 1
  << n Left shift n places
  >> n Right shift n places

## Slide 6: Bitwise operations
Bitwise operations are considered "low-level" programming by today's standards. For many programs, manipulating individual bits is never necessary.
Sometimes, this level of control is needed for memory or performance optimization
In any case, it is very important for a conceptual understanding of programming

## Slide 7: Bitwise examples: AND(&)
Bitwise AND:
Char j = 11; char k = 14;
  j: 0 0 0 0 1 0 1 1
  k: 0 0 0 0 1 1 1 0
  ---------------------
  0 0 0 0 1 0 1 0 = 10

## Slide 8: Bitwise examples: OR(|)
Bitwise OR:
Char j = 11; char k = 14;
  j: 0 0 0 0 1 0 1 1
  k: 0 0 0 0 1 1 1 0
  ---------------------
  0 0 0 0 1 1 1 1 = 15

## Slide 9: Bitwise examples: XOR(^)
Bitwise XOR:
Char j = 11; char k = 14;
  j: 0 0 0 0 1 0 1 1
  k: 0 0 0 0 1 1 1 0
  ---------------------
  0 0 0 0 0 1 0 1 = 5

## Slide 10: Bitwise examples: NOT(~)
Logical invert(NOT):
Char j = 11;
  j: 0 0 0 0 1 0 1 1
~j: 1 1 1 1 0 1 0 0 = 244

## Slide 11: Bitwise Shift Operators
• The bitwise shift operators are:
<< left shift
>> right shift
• The expression i << j represents i shifted left j positions, zero-filled.
• The expression i >> j represents i shifted right j positions. If i is of an unsigned type or if the value of i is not negative, then zero bits are added at the left as needed. If i is negative, the result depends on the implementation.

## Slide 12: Bitwise examples: Shift
Shifting
char j = 11;
  j << 1: 0 0 0 1 0 1 1 0 = 22
  j >> 1: 0 0 0 0 0 1 0 1 = 5

## Slide 13: Bitwise operation & Implementation: Shift
While(1)
{
  For(int i=0;i<=7;i++)
    {
    PORTA= PORTA&(0b00000001<<i);
    }
}

## Slide 14: Bitwise operation & Implementation: Shift
While(1)
{
  For(int i=0;i<=7;i++)
    {
    PORTA= PORTA&(0b00000001<<i);//i=0
    //(0b00000001<<0)
    // 00000001
    }
}

## Slide 15: Bitwise operation & Implementation: Shift
While(1)
{
  For(int i=0;i<=7;i++)
    {
    PORTA= PORTA&(0b00000001<<i);//i=2
    //(0b00000001<<2)
    // 00000100
    }
}

## Slide 16: Bitwise operation & Implementation: Shift
While(1)
{
  For(int i=0;i<=7;i++)
    {
    PORTA= PORTA&(0b00000001<<i);//i=3
    //(0b00000001<<3)
    // 00001000
    }
}

## Slide 17: Bitwise operation & Implementation: Shift
While(1)
{
  For(int i=0;i<=7;i++)
    {
    PORTA= PORTA&(0b00000001<<i);//i=4
    //(0b00000001<<4)
    // 000010000
    }
}

## Slide 18: Base Representation
Base 10 is default
Base can be specified with a prefix before the number
Binary is 0b, Hexadecimal is 0x
  Ex. char x = 0b00110011;
  char x = 0x33;
Binary is useful to show each bit value
Hex is compact and easy to convert to binary
  1 hex digit = 4 binary digits

## Slide 19: Bit Masks
Need to access a subset of the bits in a variable
  Write or read
Masks are bit sequences which identify the important bits with a ‘1’ value
Ex. Set bits 2 and 4 in X, don’t change other bits
  X = 01010101, mask = 0010100
  X = X | mask
Ex. Clear bits 2 and 4
  mask = 11101011
  X = X & mask

## Slide 20: Bit Assignment Macros
A macro is a fragment of code which has been given a name. Whenever the name is used, it is replaced by the contents of the macro.
#define PI 3.1415926
#define max(x,y) ((x>y) ? x:y);
you don't have to specify types in the macro definition
Function | Macros
Function is Compiled Type Checking is Done Code Length remains Same No side Effect Speed of Execution is Slower During function call, Transfer of Control takes place Useful where large code appears many time Function Checks Compile Errors | Macro is Preprocessed No Type Checking Code Length Increases Use of macro can lead to side effect Speed of Execution is Faster Before Compilation macro name is replaced by macro value Useful where small code appears many time Macro does not Check Compile Errors

## Slide 21: Bit Assignment Macros
1 << (n) and ~(1) << (n) create the mask
  Single 1 (0) shifted n times
Macro doesn’t require memory access (on stack)
#define SET_BIT(p,n) (p |= (1 << (n)))
#define CLR_BIT(p,n) (p &= (~(1) << (n)))

## Slide 22: User defined Function
  #include<avr/io.h>
  void main()
  {
  DDRA|=0xFF;
  while(1)
  {
  for(char i=0;i<=7;i++)
  {
  PORTA=1<<i;
  _delay_ms(500);
  }
  }
  }

## Slide 23: User defined Function
  #include<avr/io.h>
  Void ledBlink();
  void main()
  {
  DDRA|=0xFF;
  while(1)
  {
  ledBlink();
  }
  }
  Void ledBlink()
  {
  for(char i=0;i<=7;i++)
  {
  PORTA=1<<i;
  _delay_ms(500);
  }
  }

## Slide 24: Library
Libaries consist of a set of related functions to perform a common task;

## Slide 25: Header Files
Files included at the top of a code file
Traditionally named with .h suffix
Include information to be shared between files
  Function prototypes
  externs of global variables
  Global #defines
Needed to refer to libraries

## Slide 26
Next Lecture 7-segment display:
Next Lecture ADC:
http://maxembedded.com/2011/06/the-adc-of-the-avr/